## Slide 1
Rubber Check Investigate Result
(Using Cravis mini)
Investigate result
I
II
III
Next plan
Overview
IV
Schedule
PIC : Visual Group
Dept: AED

## Slide 2
1.1. Purpose of project
I. OVERVIEW
Check direction of rubber
Combine with others unit  Auto system
Target : Auto check after assembly
New strategy : Using Cravis mini to check
1
2
3
4
Roller
Rubber
Pi Camera
Lamp
1.2. Concept

## Slide 3
Pi Camera
50-200 mm
Cycle time of machine : 6s/pcs
Time check of Cravis : 3s/pcs
I. OVERVIEW
Pi Camera
100-300 mm
50-200mm
1.2. Concept
100-300 mm

## Slide 4
2.1. Algorithm for checking
Extract Color ( Filter Color )
White Balance
Particle (Using to searching abnormal points)
0
255
Average – threshold
Average + threshold
Average
Keep color
Convert to black
Convert to white
Count Pixel
NG pcs : 32- 75 (pixel)
OK pcs : 160-325 (pixel)
NG
OK
II. INVESTIGATE RESULT
! This is only Test Data (investigate room)

## Slide 5
II. INVESTIGATE RESULT
Sample Item check | Picture | 
 | NG sample | OK sample
Origin |  | 
Analyzed |  | 
Check Result | NG (Count pixel : 32-75) | OK (Count pixel : 160-325)
2.2. Result (300pcs)

## Slide 6
III. NEXT PLAN
3.1. Current system
3.2. Next plan
Test with many project
3.2.1 PCB
3.2.2 MOLD
3.2.3 ASSY
Blur
Hardware : small  easy to layout
Software :
Good point
Program : simple Need add more algorithms
Only check simple function Improve to check complex function
Need improve point
same with EOS program  familiar
same with industrial Camera Program
 simple, convenient, easy make new program and setup spec file

## Slide 7
IV. SCHEDULE
Work content | Mar |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Apr
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 
Test rubber (500 pcs) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | PCB
Setup in line |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Take Data |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Debug |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test 1st |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test 2nd |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test 3rd |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Apply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8
Thanks you for your attention
and valuable questions